## Slide 1: MICROSPHERE
Microsphere is a bluetooth synth controller, designed to familiarize with diatonic major harmony.

## Slide 2: WHAT WILL BE DISCUSSED trovare modo di dirlo
Why microsphere
How microsphere
Features

## Slide 3: INTRODUCTION
The foundamental need for a musician is to learn how to express himself, how to transmit to an audience what he’s feeling. There are several key skills to achieve, MicroSphere works on one of them: get used on how notes, [and scales,] sound on different chords. Interface is design to keep the process slightly more entertaining than playing single notes, or pattern, on a piano.

## Slide 4: BASED ON SCALE BRIGHTNESS
Literature tells that in diatonic major harmony a quality for perceived mood of scales can be defined: brightness. Scales can be ordered, from darkest to brightest as: locrian, phryigian, aeolian, dorian, mixolydian, ionian, lydian. In MicroSphere the darkest mode is on the lowest position of the wrist, as intuition suggests. The algorithm gives the user the two darkest modes matching the (quadriad) chord that is being played. The idea is to [facilitate the exploring] of the more exotic spices of major harmony, often left unexplored by amateur musicians.

## Slide 5: PROCEDURE I
A chord (quadriad) is played on a MIDI keyboard;
MIDI notes are scanned, finding distances between the root, supposed in first position, and other components consequently finding the type of the chord;
Intervals found are confronted with sets of diationic major harmony scales;
Matches are ordered in brightness;
Two darkest scales from X octave to Y octave are returned.

## Slide 6: CODE DIVISION
BLE connection routine;
PROCEDURE I;
Returned scales are associated to Microbit’s accelerometer values;
Accelerometer values are mapped on 3 axis: side up is forced to be necessary for mapping, tilting is associated to notes, pitching is associated to scale changes;
Mapped accelerometer values trigger WAPI synthetiser;
Interface reacts on synth and scales behaviour.

## Slide 7: ENVIRONMENT
Languages used for coding are: javascript, css and html5.
Google Chrome is the environment in which the app runs. Google’s browser is the only one supporting experimental browser features, needed for BLE connection;
Firmware in Microbit is the Lancaster University one, developers of the microprocessor.

## Slide 8: WAPI SYNTHETISER
Schema a blocchi, in sintesi: spiegazione blocchi e allacciamenti
Parameters can be modified on screen. Elenco parameters magari rimandando nella INTERFACE seconda pagina

## Slide 9: INTERFACE
Wide screen: where melodic contour is visualized. Head of trace dimension varies on wrist postion, associated with scale brightness. Head of trace position depends on note’s keyboard position. Trace (and interface color?) depend on selected scale.
«Search device» button: BLE connection routine begins;
«Start» button: melodic contour visualization begins;
«Reset» button: melodic contour visualization resets;
«MIDI» led: on if MIDI notes are received from keyboard;
«Fullscreen» button: wide screen goes full screen;

## Slide 10: INTERFACE
A keyboard from X octave to Y octave displays which piano notes are played.
INTERFACE: CONTROL PANEL
Elenco parametri synth e ultrabreve spiegazione

## Slide 11: MANCANO
BLE descrizione breve
Synth schema blocchi e spiegaz
Control panel del synth
Ottave X, Yin cui si suona
Divisione tra CM e ACTAM parts necessaria? E obiettivi? O sono già chiari così?
Aggiunte interface?
Correzioni testo slide